M A T E R I A L   S A F E T Y   D A T A   S H E E T

Page: 1

9/24/2010

========== SECTION I  -  CHEMICAL PRODUCT AND COMPANY IDENTIFICATION

PRODUCT NAME: BARGE ALL PURPOSE CEMENT: DC001 & DC031

RECOMMENDED USE: Adhesive

MANUFACTURER'S NAME: Slocum Adhesives Corp.

ADDRESS            : 2500 Carroll Avenue

Lynchburg, VA  24501

EMERGENCY PHONE    : 800-424-9300 (CHEMTREC)       DATE PRINTED  : 9/24/2010

INFORMATION PHONE  : 434-847-5671

========== SECTION II - HAZARD IDENTIFICATION

DANGER! Flammable liquid.  Irritant by inhalation, ingestion, skin contact, eye

contact.

ROUTES OF ENTRY

Inhalation, skin absorption, ingestion.

INHALATION HEALTH RISKS AND SYMPTOMS OF EXPOSURE

Breathing high concentrations of vapors may cause irritation of the nose and

throat or signs of nervous system depression (i.e. - headache, nausea,

drowsiness, dizziness, vomiting, loss of coordination and fatigue).

EYE CONTACT HEALTH RISKS AND SYMPTOMS OF EXPOSURE

May cause mild eye irritation.  Direct contact with liquid or vapors may cause

stinging, tearing, redness, swelling, and eye damage.

SKIN ABSORPTION HEALTH RISKS AND SYMPTOMS OF EXPOSURE

This material may cause mild skin irritation.  Prolonged or repeated contact or

exposure to vapors may cause redness, burning, and drying and cracking of the

skin.

INGESTION HEALTH RISKS AND SYMPTOMS OF EXPOSURE

Ingestion may cause irritation of the digestive tract, nausea, vomiting, and

signs of nervous system depression.

MEDICAL CONDITIONS GENERALLY AGGRAVATED BY EXPOSURE:

Pre-existing eye, skin, or respiratory disorders may be aggravated by exposure

to this product.

========== SECTION III  -  COMPOSITION / INFORMATION ON INGREDIENTS

REPORTABLE COMPONENTS              CAS NUMBER   VAPOR PRESS.        WT. %

-----------------------------------------------------------------------------------------------------------------------------------------

* Toluene                          108-88-3        22.4           50 - 75%

OSHA PEL: 200 ppm

ACGIH TLV:  50 ppm TWA

Heptane                            142-82-5        36.4           12 - 25%

OSHA PEL: 500 ppm

ACGIH TLV:  400 ppm TWA

Ethyl Acetate                      141-78-6        73.1           5 - 15%

M A T E R I A L   S A F E T Y   D A T A   S H E E T

Page: 2

9/24/2010

OSHA PEL: 400 ppm

ACGIH TLV:  400 ppm TWA

*  Indicates toxic chemical(s) subject to the reporting requirements of section

313 of Title III.

========== SECTION IV  -  FIRST AID MEASURES

EMERGENCY AND FIRST AID PROCEDURES:

SKIN: In case of contact, immediately flush skin with plenty of soap and

water for at least 15 minutes.  Remove contaminated clothing and wash

affected areas thoroughly with mild soap.  If irritation develops, seek

medical attention.

EYES: In case of contact, immediately flush eyes with plenty of water for

at least 15 minutes and get medical attention if irritation persists.

INHALATION: If inhaled, remove to fresh air.  If not breathing, give

artificial respiration, preferably mouth-to-mouth.  If breathing is

difficult, give oxygen.  Get medical attention.

INGESTION: Get medical attention.  If vomiting occurs, keep head lower

than hips to prevent aspiration.

========== SECTION V  -  FIRE FIGHTING MEASURES

FLASH POINT(°F): 21                     METHOD USED: TCC

FLAMMABLE LIMITS IN AIR (% BY VOL):  LOWER: 1.00       UPPER: 11.60

EXTINGISHING MEDIA: Carbon dioxide, Dry chemicals, Foam.

SPECIAL FIREFIGHTING PROCEDURES

May produce toxic fumes if burning.  The use of self-contained breathing

apparatus is recommended for fire fighters.  Water may be unsuitable as an

extinguishing medium, but helpful in keeping adjacent containers cool; avoid

spreading the liquid with water used for cooling.

========== SECTION VI  -  ACCIDENTAL RELEASE MEASURES

Keep sources of ignition isolated from spill.  Stop spill/release if it can be

done without risk.  Wear appropriate protective equipment including respiratory

protection as conditions warrant and stay upwind.  Prevent material from

entering sewers, storm drains, or other natural waterways.  Dike far ahead of

spill for later recovery or disposal.  Spilled material may be absorbed into an

appropriate absorbent material.  Immediate clean-up of any spill is recommended.

Notify fire authorities and appropriate federal, state, and local agencies.

========== SECTION VII  -  HANDLING AND STORAGE

PRECAUTIONS TO BE TAKEN IN HANDLING AND STORING

Avoid extremes of heat or cold.  Keep product containers closed when not in use.

M A T E R I A L   S A F E T Y   D A T A   S H E E T

Page: 3

9/24/2010

Use and store material in well-ventilated areas away from open flames, heat, hot

metal surfaces, and other potential sources of ignition.  Bond and ground

equipment when transferring from one vessel to another.  Store only in approved

containers.  Personal contact and inhalation should be avoided. Wash hands after

use.  Do not eat, drink, or smoke in work area.

========== SECTION VIII  -  EXPOSURE CONTROLS / PERSONAL PROTECTION

See Section III for exposure limits of hazardous ingredients.

RESPIRATORY PROTECTION:

Use approved NIOSH respiratory protection if TLV is exceeded or if overexposure

is likely.

VENTILATION:

Mechanical ventilation.

PROTECTIVE GLOVES:

Impermeable gloves.

EYE PROTECTION:

Wear safety glasses or goggles to protect against exposure.

OTHER PROTECTIVE CLOTHING OR EQUIPMENT:

May use impermeable apron as needed, eye washes, and safety showers.

========== SECTION IX  -  PHYSICAL AND CHEMICAL PROPERTIES

APPEARANCE: Yellow liquid.              ODOR: Solvent odor.

pH: Not available.                      ODOR THRESHOLD: Not available.

MELT/FREEZE POINT(°F): No data.         BOILING POINT(°F): 172

FLASH POINT(°F): 19                     EVAPORATION RATE: Faster than nBuAc.

FLAMMABILITY (SOLIDS, GAS)N/A.          LOWER FLAM. LIMIT: 1.00

VAPOR DENSITY: Heavier than air.        UPPER FLAM. LIMIT: 11.60

VAPOR PRESSURE: Refer to Section III for vapor pressure values.

SPECIFIC GRAVITY: .8796                 WEIGHT PER GAL.: 7.3244 lb/gl

SOLUBILITY IN WATER: Insoluble.

PARTITION COEFFICIENT (n-octanol/water): No data.

AUTO-IGNITION TEMP.(°F): No data.

DECOMPOSITION TEMP. (°F): No data.

VOLATILE (WT.%): 75.7946%               VOC CONTENT: 664 g VOC/L PRODUCT

========== SECTION X  -  STABILITY AND REACTIVITY

STABILITY:

Stable.

CONDITIONS TO AVOID:

Avoid extremes of heat or cold.

INCOMPATIBILITY (MATERIALS TO AVOID):

Incompatible with alkali metals, halogens, and strong acids or bases.

HAZARDOUS DECOMPOSITION OR BYPRODUCTS:

Carbon monoxide, carbon dioxide, smoke, and other unidentified organic compounds

may be formed during combustion.

HAZARDOUS POLYMERIZATION:

Will not occur.

========== SECTION XI - TOXICOLOGICAL INFORMATION

See Section II for additional information regarding health risks.

M A T E R I A L   S A F E T Y   D A T A   S H E E T

Page: 4

9/24/2010

CARCINOGENICITY:  NTP CARCINOGEN: No.

IARC MONOGRAPHS: No.

OSHA REGULATED: No.

REPRODUCTIVE TOXICITY: No data.

MUTAGENICITY: No data.

STOT-single exposure: No data.

STOT-repeated exposure: No data.

ASPIRATION HAZARD: No data.

METHYLENE CHLORIDE?: Methylene chloride is not present in this product.

========== SECTION XII - ECOLOGICAL INFORMATION

AQUATIC TOXICITY: ACUTE AND PROLONGED TOXICITY TO FISH: No data.

ACUTE TOXICITY TO AQUATIC INVERTEBRATES: No data.

ENVIRONMENTAL FATE AND PATHWAYS: No data.

========== SECTION XIII - DISPOSAL CONSIDERATIONS

Dispose of in accordance with all applicable local, state, and federal

regulations.  Do not discharge effluent containing this product into lakes,

streams, ponds, estuaries, oceans, or other waters unless in accordance with the

requirements of a National Pollutant Discharge Elimination System (NPDES)

permit, and the permitting authority has been notified in writing prior to

discharge.  Do not discharge effluent containing this product to sewer systems

without previously notifying the local sewage treatment plant authority.  For

guidance, contact your State Water Board or Regional Office of the EPA.

========== SECTION XIV - TRANSPORTATION INFORMATION

NOTE: The assignment of Proper Shipping Name is in part a function of the size

of the product container and the transport mode.  For example, the Proper

Shipping Name for a bulk container can differ significantly from the Proper

Shipping Name for the same product packaged in a non-bulk container.  This can

also be true for products shipped via different modes of transportation (i.e.

ground, air, ocean).  The descriptions provided here are intended to provide

some guidance. However, these descriptions may not apply to your package size or

mode of shipment.

The U.S. Code of Federal Regulations, 49 CFR - Transportation, regulations, and

the policies established by some transporters, require that the shipper properly

classify and assign a Proper Shipping Name, and label, mark and package the

material properly.  Therefore, the user of this information is cautioned to

consult with applicable regulations, and with qualified advisors prior to the

repackaging and/or reshipment of this or any other product which contains this

product.

SMALL QUANTITY (1 gallon or less):

ORM-D; CONSUMER COMMODITY

DOT (ROAD, RAIL, WATER):

PROPER SHIPPING NAME:  ADHESIVES; UN1133; PG II; CLASS 3

IMDG (ROAD, RAIL WATER):

PROPER SHIPPING NAME:  ADHESIVES; UN1133; PG II; CLASS 3

M A T E R I A L   S A F E T Y   D A T A   S H E E T

Page: 5

9/24/2010

========== SECTION XV - REGULATORY INFORMATION

NFPA CODES:  H F R P

2 3 0 B

CALIFORNIA PROPOSITION 65

WARNING! This product contains the following substance(s) known to the state of

California to cause birth defects or other reproductive harm.

TOLUENE

========== SECION XVI - OTHER INFORMATION

The information contained herein is based on the data available to us and is

believed to be correct.  However, Slocum Adhesives Corporation makes no

warranty, expressed or implied, regarding the accuracy of these data or the

results to be obtained from the use thereof.  Slocum Adhesives Corporation

assumes no responsibility for injury from the use of the product described

herein.